## Slide 1
Benchmark Optimization, Analysis, and Hardware Acceleration
pyperformance N-body and Pyflate | Course QEMU measurements
Software correctness, profiling, optimization, and synthesizable RTL

## Slide 2
Method and success criteria
HWSW project | N-body and Pyflate | 2
Two approved workloads: N-body and Pyflate
Understand algorithms and data structures before changing code
Measure with rigorous pyperf on one pinned QEMU vCPU
Locate hotspots with Linux perf and flame graphs
Require identical output/state and at least 7% improvement
Propose explicit ready/valid hardware interfaces and software fallback

## Slide 3
Experimental environment and correctness
HWSW project | N-body and Pyflate | 3
Ubuntu 5.15.0-1106-kvm under KVM
1 vCPU: Intel Xeon E5-2630 v3 at 2.40 GHz
CPython 3.10.12; pyperformance 1.14.0; pyperf 2.10.0
N-body: complete positions, velocities, and energy matched
Pyflate: 399,360 output bytes matched byte-for-byte
Pyflate MD5: afa004a630fe072901b1d9628b960974
Both SystemVerilog self-checking simulations passed

## Slide 4
N-body: workload and baseline
HWSW project | N-body and Pyflate | 4
Five solar-system bodies; ten unordered interaction pairs
20,000 dependent time steps per benchmark operation
Per pair: displacement, inverse distance cubed, two velocity updates
Per step: integrate all five positions
Complexity: O(T*N^2); N is fixed, so CPython overhead dominates
Baseline storage: nested Python lists/tuples and boxed float objects

## Slide 5
N-body baseline profile
29,396 CPU-clock samples; zero lost samples
HWSW project | N-body and Pyflate | 5
43.54% CPython frame evaluation
7.09% float creation
5.49% generic binary dispatch
3.46% float multiplication
2.88% list assignment
Only 2.03% in inverse-distance pow

## Slide 6
N-body software optimization
HWSW project | N-body and Pyflate | 6
Store positions, velocities, and masses in dense NumPy float64 arrays
Compile the complete pair and integration loops with Numba nopython
Warm compilation before timing; measure cold start separately
Keep pair order, update order, float64, and fast-math disabled
Return an energy checksum so the computation remains observable
Result: remove interpreter dispatch and expose the true math hotspot

## Slide 7
N-body result: 23.13x faster
HWSW project | N-body and Pyflate | 7
Baseline
230 ms
Optimized
9.94 ms
95.68% time reduction; required threshold: 7%
120 values each; CV 1.60% baseline and 2.52% optimized
Optimized profile: CPython evaluation falls from 43.54% to 0.01%
Power-related functions become about 70.25% of execution
Cold import + compilation: 1.288 s; break-even near six operations

## Slide 8
N-body hardware proposal and limits
HWSW project | N-body and Pyflate | 8
Q16.16 pair-force datapath; Q2.30 host-provided inverse distance cubed
One-cycle ready/valid reference; equal-and-opposite saturated outputs
Standalone PCIe offload is not viable for only ten dependent pairs/step
Production design must add reciprocal square root, accumulation, and multi-step residency
At P=70.25% and S=20, ideal Amdahl bound is about 3.0x before transfer cost

## Slide 9
Pyflate: workload and baseline
HWSW project | N-body and Pyflate | 9
Pure-Python BZip2 decode of interpreter.tar.bz2
Bit extraction -> canonical Huffman -> MTF/RLE -> inverse BWT
Baseline reads one byte per method call
Huffman decode linearly scans code objects for every symbol
Bit masks are reconstructed repeatedly
Move-to-front rebuilds lists through slicing and concatenation

## Slide 10
Pyflate baseline profile
47,455 CPU-clock samples; zero lost samples
HWSW project | N-body and Pyflate | 10
23.31% CPython frame evaluation
4.09% allocator address checks
2.88% allocation-size reads
2.54% list deallocation
2.14% list slicing
1.14% list concatenation

## Slide 11
Pyflate software optimization
HWSW project | N-body and Pyflate | 11
Read compressed input once into a contiguous bytes buffer
Index bytes directly and cache masks for widths 0 through 64
Group canonical codes by valid bit length
Use O(1)-average dictionary lookup instead of scanning code objects
Replace move-to-front slicing with in-place pop and insert
Keep block parsing, Huffman semantics, MTF/BWT/RLE, and output unchanged

## Slide 12
Pyflate result: 1.43x faster
HWSW project | N-body and Pyflate | 12
Baseline
1.121 s
Optimized
0.782 s
30.26% time reduction; required threshold: 7%
120 values each; CV below 1% for both runs
Total samples fall 27.2%
Absolute CPython evaluation time falls about 22%
List-slice sample count falls about 97%; concatenation is no longer significant

## Slide 13
Pyflate hardware proposal
HWSW project | N-body and Pyflate | 13
Programmable 1-20 bit canonical-Huffman lookup with explicit errors
32-bit normalized window; symbol and consumed-bit ready/valid output
BZip2 bytes are bit-reversed by the stream packer for transmission order
Production design banks all six BZip2 tables to avoid reprogramming
Conditional P=0.50, S=10 Amdahl estimate: 1.82x before DMA overhead

## Slide 14
Hardware trade-offs and integration
HWSW project | N-body and Pyflate | 14
Batch commands; never pay MMIO/PCIe latency per Python operation
Keep tables and intermediate state resident across many symbols/steps
Q16.16 reduces area/power but needs range checks and numerical validation
Parallel Huffman compare gives throughput but costs comparator area and power
Banked SRAM/prefix tables reduce area at the cost of extra latency
Every unsupported range, malformed table, or error returns to verified software
100-200 MHz targets are assumptions; no synthesis or power result is claimed

## Slide 15
What the measurements taught us
HWSW project | N-body and Pyflate | 15
N-body: interpreter removal exposes inverse-distance power as the new bottleneck
Pyflate: fewer method calls and temporary lists improve both time and locality
Algorithmic and data-layout changes should precede hardware
Amdahl's law and transfer overhead bound accelerator value
Debug-symbol perf profiles are useful, but unresolved VM/JIT frames must be disclosed
Correctness evidence and raw measurements are as important as headline speedup

## Slide 16
Conclusion
HWSW project | N-body and Pyflate | 16
N-body: 23.13x faster, 95.68% less time, identical validated state
Pyflate: 1.43x faster, 30.26% less time, byte-identical output
Both exceed the required 7% improvement
Both RTL designs pass self-checking simulation
Hardware proposals define interfaces, fallback, and realistic limitations
All scripts, raw JSON, perf reports, flame graphs, RTL, and prompts are reproducible